Parity Check
In parity, you just add a parity bit to the data word that you wish to send. The value of the parity bit should make the total number of 1's in the data word even. Thus, if there are even number of 1's in the original data word, the parity bit should be 0, 1 otherwise.
On the receiving end, you just count the number of 1's in the received data word. If it is odd then there is an error.

def append_even_parity(self):
        self.is_even_parity = True
        ones = self._count_ones(self.bits)
        if ones % 2 == 0:
        self.bits.append(0)
        else:
        self.bits.append(1)
        return self.bits

def detect_error(self):
        ones = self._count_ones(self.received)
        if self.is_even_parity:
        return ones % 2 == 0
        else:
        return ones % 2 == 1

Hamming Code
The hamming code we built is a single-bit-error-correction code. Our data word is of length 4, thus requiring 3 parity bits. Therefore, we have a code word of length 7 bits.
The code word has the format:
Dataword[3]	Dataword[2]	Dataword[1]	Dataword[0]	Parity[2]	Parity[1]	Parity[0]

Parity[0] = (dataword[2] + dataword[1] + dataword[0]) % 2
Parity[1] = (dataword[3] + dataword[2] + dataword[1]) % 2
Parity[2] = (dataword[1] + dataword[0] + dataword[3]) % 2

On the receiving end, we need to compute for the syndrome. The length of the syndrome is the same as the number of parity bits.
Syndrome[0] = (dataword[2] + dataword[1] + dataword[0] + parity[0]) % 2
Syndrome[1] = (dataword[3] + dataword[2] + dataword[1] + parity[1]) % 2
Syndrome[2] = (dataword[1] + dataword[0] + dataword[3] + parity[2]) % 2
The syndrome is writen in the form 'Syndrome[2]Syndrome[1]Syndrome[2]'. To detect which bit has the error, we use the table below:
Syndrome	000	001	010	011	100	101	110	111
Error	None	parity[0]	parity[1]	dataword[2]	parity[2]	dataword[0]	dataword[3]	dataword[1]

After getting the syndrome, just identify which part of the code word has an error and invert its value.

def add_parity_bits(self):
        r0 = (self.bits[3] + self.bits[2] + self.bits[1]) % 2
        r1 = (self.bits[2] + self.bits[1] + self.bits[0]) % 2
        r2 = (self.bits[3] + self.bits[2] + self.bits[0]) % 2
        self.bits += [r2, r1, r0]
        return self.bits

def correct_error(self):
        s0 = (self.received[1] + self.received[2] + self.received[3] +
        self.received[6]) % 2
        s1 = (self.received[0] + self.received[1] + self.received[2] +
        self.received[5]) % 2
        s2 = (self.received[0] + self.received[2] + self.received[3] +
        self.received[4]) % 2
        coding = {
        '000': -1,
        '001': 6,
        '010': 5,
        '011': 1,
        '100': 4,
        '101': 3,
        '110': 0,
        '111': 2
        }
        syndrome = '{0}{1}{2}'.format(s2, s1, s0)
        print 'syndrome = ' + syndrome
        index = coding[syndrome]
        if index == -1:
        print "No error"
        else:
        if self.received[index] == 0:
        self.received[index] = 1
        else:
        self.received[index] = 0
        print 'Data code after correction: %r' % self.received[0:4]
        return self.received[0:4]

Burst Error Correction
The technique of burst error correction is to divide the data word into several data words and generate code words using hamming code. In our case, we had the original data word 12 bits long. We divided it into 3 data words each of length 4 bits. Each data word was transformed into code words using hamming code. Now we have 3 code words each of length 7 bits. In transmitting, we don't transmit code word by code word. We transmit bit by bit. We first transmit the 1st bit of the 1st code word, then the 1st bit of the 2nd code word, then the 1st bit of the 3rd code word, then the 2nd bit of the 1st code word, then the 2nd bit of the and so on.
On the receiving end, we need to recover the code words. After recovering the code words, we use hamming code error correction for each code word and recover the original data word.

def initialize_hamming_code(self):
        self.hamming = []
        length = len(self.bits)
        hamming_count = length / 4
        print "Code words using hamming code:"
        for i in range(0, hamming_count):
        hamming = HammingCode(bits=self.bits[i * 4: (i + 1) * 4])
        hamming.add_parity_bits()
        print hamming.bits
        self.hamming.append(hamming)

def simulate_send(self):
        self.sent = []
        code_word_length = len(self.hamming[0].bits)
        for i in range(0, code_word_length):
        for h in self.hamming:
        self.sent.append(h.bits[i])
        print "Sent code words: \n %r" % self.sent
        return self.sent

def correct_error(self):
        code_word_length = len(self.hamming[0].bits)
        hamming_count = len(self.hamming)
        for index, d in enumerate(self.received):
        self.hamming[index % hamming_count].received.append(d)
        self.retrieved_data = []
        for h in self.hamming:
        print "received hamming code: %r" % h.received
        corrected = h.correct_error()
        self.retrieved_data += corrected
        print self.retrieved_data
        return self.retrieved_data